## Slide 1: Impact Assessment of Irrigation Development in the Tana Basin on Beles Hydropower and Lake Navigation
Deksyos Tarekegn
National DSS Specialist - Ethiopia

## Slide 2: Background
The Tana & Beles sub-basins are located in the Blue Nile Basin.
Tana:
  15,083sqkm including Lake area of 3000sqkm.
  Gross storage 32 BCM; Live 8.5BCM
  Source of Blue Nile
Beles:
  13,573 sqkm
  The last tributaries of Blue Nile in Ethiopia
Elevation ranges from 4100 – 500masl

## Slide 3: Background
Tana basin Gauged Area 42 %
Beles only 29 % is gauged
MAF
  Tana outflow 3753MCM
  Beles MAF: 4900MCM
Since 2010 the two S-basins are connected through 12 km tunnel to transfer water to from L. Tana to generate HP (460MW

## Slide 4: Existing Developments
Tana-Beles Transfer Tunnel
Chara-Chara Weir
Koga Dam
 | Storage Capacity, mcm | Irrigated area, ha | HP Installed Capacity, mw | Remark
Tana Basin |  |  |  | 
Chara-Chara weir | 32,000 (Lake Tana) |  |  | At the outlet of the Lake Tana
Koga Dam & Irrigation | 170.5 | 7,000 |  | 
Tis-Abbay I and II Hydropower |  |  | 84 | Currently, these plants are operated as standby
Beles Basin |  |  |  | 
Beles Hydropower |  |  | 460 | 
Total |  | 7,000 | 460 | 
Navigation: Lake Tana is used for Navigation, a basic transport to the residents of islands and lake peripheries.
Fishery: L. Tana has huge Fish potential

## Slide 5: Development Potential
 | Storage mcm | Irrigable area, ha | HP, mw | Remark
Tana Basin |  |  |  | 
Megetch Dam & Irrigation | 181.8 | 7,311 |  | 
Ribb Dam & irrigation | 233.7 | 18,700 |  | 
Gilgel Abbay dam & Irrigation | 365.8 | 14,552 |  | 
Jema dam &Irrigation | 124.1 | 7,786 |  | 
Gumara & irrigation | 223 | 14,000 |  | 
All Lake Tana pumping Irrigation |  | 44,650 |  | 
Gonder Town water supply |  |  |  | Pumping from Megetch dam,
Beles Basin |  |  |  | 
Upper Beles Irrigation |  | 54,000 |  | 
Dangur Hydropower |  |  | 168 | 
Lower Beles Irrigation |  | 85,000 |  | 
Total |  | 246,000 | 168 | 
Tana: 114,000 ha
Beles: 139,000 ha

## Slide 6: Key Questions
What will be the impact of irrigation development in the Tana basin on the Beles Hydropower generation?
By how much the Lake level will be reduced, and what would be the impacts on the navigational use of Lake Tana?
What will be the change in Beles flow to Blue Nile?
To address the above key questions , MIKE BASIN model is used.
The following key indicators are used:
  Time series of hydropower generation
  Time series of lake water level
  Amount of irrigation water abstracted and deficiency
  Time series of Beles flow

## Slide 7
MIKE BASIN is a simulation model for water allocation representing the hydrology of the basin in space and time.
It is a network model in which the rivers and their main tributaries are represented by a network of branches and nodes
GIS based software build as an ARCGIS extension
Main areas of Applications:
  Water allocation and scenario modeling
  Reservoir/Hydropower operation
  Hydrological modeling
  Irrigation demand and Yield assessment
  In-stream nutrient modeling
  Catchment nutrient load assessment
  TS data management and analysis
Mike Basin
A multi purpose modeling and data management system for Integrating and River basin management

## Slide 8: Data Availability
  Hydrological Study of the Tana-Beles Sub-Basins, SMEC 2008
    Runoff depths at sub-catchments level, 1960-2005, at monthly time step
    Rainfall (monthly) and evaporation (mean monthly) over the lake
  Abbay Master plan Report; Identifying potential projects.
  Feasibility, pre-feasibility and reconnaissance studies of the dams and Irrigation development project.
Notes: 8

## Slide 9: Scenario Definition
Development Interventions | Scenario 0 | Scenario 1 | Scenario 2 | Scenario 3
 | Baseline (Existing) | Medium scale development | Large scale development | Full scale development
Chara-Chara weir | X | X | X | X
Beles Hydropower (460MW) | X | X | X | X
Koga Dam & Irrigation (7,000ha) | X | X | X | X
Megetch Dam & Irrigation (7,311ha) | -- | X | X | X
Ribb Dam and irrigation (18,700ha) | -- | X | X | X
Upper Beles Irrigation(54,000ha) | -- | X | X | X
Gonder Town Water supply | -- | X | X | X
Gilgel Abbay dam & Irrigation (14,552ha) | -- | -- | X | X
Jema dam and Irrigation (7,786ha) | -- | -- | X | X
Gumara dam & irrigation (14,000ha) | -- | -- | X | X
Dangur Hydropower (168MW) | -- | -- | X | X
Lower Beles Irrigation(85,000ha) | -- | -- | X | X
Lake Tana pumping Irrigation (44,650ha) | -- | -- | -- | X
Total |  |  |  | 
Irrigation, ha | 7,000 | 87,011 | 208,349 | 253,000
Hydropower, mw | 460 | 460 | 628 | 628
Gonder Town water supply, mcm/year | -- | 30.3 | 30.3 | 30.3

## Slide 10: Model setup
Tana basin is divided into 16 sub-catchments, including6 dams catchments
Beles basin is divided into 4 catchments, including 3 dam catchments.
90 m DEM is used to delinete the catchments
Simulation Period: 1960-2005
Notes: 10

## Slide 11: Model Calibration
The Model in MB is calibrated to match the observed and simulated levels
The calibration is on the loss and Gains of the lake; these are the most uncertain inputs since their variation on the lake is very high
In order to avoid spills from the Chara-Chara weir during calibration, the flood control level is set very high.
The measured flow at the outlet of the lake includes total flow ( spill + release)
The existing developments considered are Chara-Chara weir, Tis-Isat power plants.
Proxy reservoir is added downstream of Chara-Chara to divert water to Tis Issat HP and to Tis-Isat falls
The average flow to Tis-Issat falls is set to 17 m3/s ( a minimum of 10 in dry months and higher in wet months)
Notes: 11

## Slide 12
Name | Maximum | Minimum | Time weighted average
Observed Level | 1787.72 | 1784.36 | 1786.100
Simulated Level | 1787.77 | 1784.37 | 1786.101
Model Calibration-Lake Level
Notes: 12

## Slide 13: Model Calibration-Lake Level
Chart: Observed Level
Scattered Diagram of Observed and Simulated Lake Level

## Slide 14: Result: Impacts on Lake Navigation
Scenario | Lake Level, masl |  | 
 | Maximum | Minimum | Median
Tana_WL_SC0 | 1787.00 | 1783.87 | 1785.90
Tana_WL_SC1 | 1787.00 | 1783.76 | 1785.73
Tana_WL_SC2 | 1787.00 | 1783.57 | 1785.41
Tana_WL_SC3 | 1787.00 | 1783.46 | 1784.99
Notes: 14

## Slide 15: Result: Impacts on Lake Navigation
The Minimum operating level of Chara-Chara weir is 1784 masl
The L.Tana transport enterprise insist that the minimum Lake level for Navigation is 1784.75 masl
In the present study the MOL is set to 1784, there is plan to try different MOLs and reduction levels and fractions.
In full development the minimum lake level drops by 41 cm from the baseline scenario
In the baseline scenario, the lake level drop below 1784.75 for about 5% of the simulation period. Whereas, in full development it drops for about 40% of the time.

## Slide 16: Result: Impacts on Beles HP generation
Chart: Time, months
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Baseline scenario | 209.8289 | 210.0169 | 209.76 | 207.9531 | 206.08 | 205.505 | 260.2307 | 258.3304 | 312.2902 | 325.3925 | 225.2123 | 209.76
Scenario-1 | 208.4347 | 208.84 | 207.3033 | 201.5017 | 200.5473 | 197.6708 | 256.6399 | 252.12 | 295.0997 | 290.0713 | 220.3506 | 207.5089
Scenario-2 | 202.3859 | 202.5948 | 198.6337 | 187.052 | 181.535 | 169.4799 | 233.214 | 238.5568 | 283.8562 | 277.711 | 210.3681 | 201.4448
Scenario-3 | 194.2492 | 190.1988 | 174.8 | 153.8275 | 137.0915 | 126.4094 | 183.8358 | 228.6126 | 251.0656 | 257.7539 | 202.4901 | 193.6744
Scenario | Unit | Maximum value | Time weighted average value
Baseline | MW | 460 | 236.8
Scenario 1 | MW | 460 | 228.9
Scenario 2 | MW | 460 | 215.7
Scenario 2 | MW | 460 | 191.2

## Slide 17
Result: Impacts on Beles HP generation
In Scenario 1 the average Beles HP generation reduced by 8 MW only
In Scenario 2 and 3, the generation decrease by 21 and 46 MW
Notes: 17

## Slide 18: Result: change in Beles outflow to Blue Nile
Chart: Time, Years
| 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004
Scenario 3 | 229.5955 | 172.2183 | 195.9769 | 228.2592 | 178.547 | 136.6275 | 189.7296 | 136.7135 | 96.0614 | 213.519 | 112.7948 | 105.7784 | 115.8323 | 200.066 | 205.7934 | 226.0848 | 225.3524 | 193.8529 | 168.3918 | 132.0891 | 141.7416 | 180.177 | 145.2799 | 144.0284 | 140.4009 | 223.1276 | 150.7484 | 168.3567 | 301.6167 | 299.2964 | 213.1865 | 128.031 | 163.213 | 212.6657 | 184.44 | 132.5394 | 235.1973 | 175.2041 | 242.6096 | 264.5062 | 273.3043 | 216.1053 | 156.3562 | 251.348 | 230.5447
Baseline | 272.91 | 221.3538 | 244.7645 | 271.7691 | 220.191 | 176.6671 | 235.4943 | 141.2556 | 183.177 | 259.6804 | 190.9984 | 177.782 | 186.556 | 279.6216 | 282.9474 | 300.0661 | 268.8213 | 248.8292 | 222.4998 | 175.4589 | 221.2451 | 260.9383 | 220.3247 | 213.9281 | 205.8526 | 281.6673 | 213.5094 | 224.6915 | 369.7205 | 346.5267 | 267.2973 | 204.8294 | 228.9749 | 263.8612 | 240.1658 | 188.8872 | 305.7447 | 230.594 | 297.9845 | 319.8338 | 317.0623 | 267.0631 | 195.7026 | 296.6987 | 278.7568
 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9 | 244.9
 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2 | 187.2
Mean Annual Flow of Beles River at the Confluence with Blue Nile.
The Beles river flow at the Blue Nile confluence is reduced from the baseline MAF of 7723mcm to 5903mcm at full development (scenario 3) i.e, the flow reduce by 1819mcm or 18.2%.

## Slide 19: Summary of Results
Indicators |  | Baseline | Scenario 1 | Scenario 2 | Scenario 3
Beles average generated Power (mega watt) |  | 236.8 | 228.9 | 215.7 | 191.2
Tana Water Level (masl) | Minimum | 1783.87 | 1783.76 | 1783.57 | 1783.46
 | Maximum | 1787 | 1787 | 1787 | 1787
 | Median | 1785.9 | 1785.73 | 1785.41 | 1784.99
Percentage of Time Lake level drops below 1784.75(minimum level for safe navigation) |  | 7.2 | 11.9 | 23.3 | 39.6
Percentage of Time Lake level drops below 1784 (minimum operating level for HP) |  | 0.4 | 0.5 | 4 | 9.8
Reliability of Gonder town water supply (%) |  | -- | 88.2 | 88.2 | 88.2
outflow to , (mcm) |  | 7723 | 7152 | 6162 | 5903
Reliability of Upper Beles Irrigation water supply |  | -- | 99.6 | 96.7 | 91.3

## Slide 20: Conclusion
In the medium scale irrigation development in the Tana Basin, SC-1, (33000ha) the lake level in almost all the time remain above 1784 masl.
In the large scale development scenario, SC-2 (69350 ha. In L. Tana basin), the Lake level drops below the designed minimum operation level of 1784, for about 4% of the time. But in full scale development the level drops for about 10% of the simulation period.
The impact on the Beles Hydropower generation is insignificant in the medium scale developments, SC-1. The average power generation is reduced by 8 MW.
In medium and full scale development scenarios, SC-2 & SC-3, there is significant impact on the Beles hydropower generation; the average annual power generation drops to 216 and 191 mw respectively from the current 237 mw.
The optimum lake level require to navigate Lake Tana is 1784.75. However, even in the baseline scenario, the lake level drops below this level for about 5 % of the time. In medium, large and full scale developments, the level drops below 1784.75 for about 12%, 23% and 40% of the time respectively. Hence, at full scale development impact on L.Tana navigation is significant with the current navigation facilities.
Notes: 20

## Slide 21
Thank You